INSTRUCTION: Select the correct answer for each of the following questions. Mark only one answer for each item by shading the box corresponding to the letter of your choice on the answer sheet provided. STRICLY NO ERASURES ALLOWED. Use pencil no. 1 only.

MULTIPLE CHOICE:

- It is the branch of physics pertaining to the phenomena and law of sound including the study of regulating sound and its reflecting properties.

- reverberation

- acoustics

- echo

- attenuation

- The person who signs and seals plans for electrical for the purpose of obtaining a building permit.

- master plumber

- professional electrical engineer

- sanitary engineer

- structural engineer

- An equipment for transporting people or things vertically or up and down the building

- escalator

- stairwell

- dumbwaiter

- elevator

- A process of treating air so as to control simultaneously its temperature, humidity, cleanliness and distribution within an interior space such as room or building.

- air conditioning

- cooling

- heating

- ventilating

- A pipe, sheet metal or conduit fitting having a bend usually 90 degrees.

- elbow

- nipple

- tee

- wye

- A duct used to transfer air from one location to another.

- aqueduct

- ductile

- viaduct

- air duct

- A water outlet valve; also called a cock.

- globe valve

- gate valve

- faucet

- union

- A unit of luminous intensity

- candela

- lumen

- brightness

- light

- A nipple having no shoulder and having the shortest possible length permitted by standard practice.

- 1” nipple

- close nipple

- open nipple

- 3” nipple

- In a plumbing system, a branch in the shape of the letter Y

- tee-wye branch

- tee branch

- wye branch

- split branch

- Color-coding of plastic pipes and fittings for electrical conduit

- red

- orange

- blue

- gray

- A power-driven, inclined continuous stairway used for raising or lowering passengers

- escalator

- stairwell

- stringer

- elevator

- What does the letter “U” in UPVC mean?

- unsaturated

- undersized

- unglazed

- unplasticized

- A low, basin-like fixture on which the user sits, used to wash the posterior parts of the body.

- urinal

- bidet

- lavatory

- slopsink

- A stream of high-velocity temperature-controlled air which is directed downward, across an opening.

- curtain wall

- air curtain

- wind

- breeze

- A unit of flow of electric current

- ampere

- voltage

- resistance

- hertz

- A valve for controlling the flow of a liquid or air at right angles to the direction in which it enters the valve.

- check valve

- globe valve

- angle valve

- gate valve

- An over-current protective device consisting of a metal strip, ribbon or wire which is designed to open an electric circuit by melting if a predetermined current is exceeded.

- cut-out

- filament

- breaker

- fuse

- An artificial reservoir or tank for storing water at atmospheric pressure such as rainwater collected from a roof for use when required

- septic tank

- catch basin

- area drain

- cistern

- A structure, usually on the roof of a building, over which water is circulated so as to cool it evaporately by contact with air

- cooling tower

- condenser

- evaporator

- radiator

- A short internally-threaded section pipe, used to join two pipes or conduits.

- flange

- connector

- nipple

- coupling

- A lamp from which light is emitted when tungsten filament is heated to incandescence by an electric current.

- fluorescent

- incandescent lamp

- tungsten

- halogen

- A device that redirects light or sound by reflection

- reflector

- filter

- filament

- dimmer

- …to circuit conductors is made

- utility box

- junction box

- panel box

- fuse box

- Elisha Graves Otis is known for the technology of

- curtain walls

- door closers

- elevators

- lifts

- What is the maximum angle of inclination of an escalator?

- 35 degrees

- 30 degrees

- 20 degrees

- 40 degrees

- The flow of electric current in a circuit expressed in amperes

- voltage

- wattage

- amperage

- resistance

- The flow of water or other liquids in a direction opposite to the natural or intended direction of flow.

- suction

- backwash

- siphonage

- splash

- A cutout box containing the fuses for an electric circuit

- circuit breaker

- panel board

- junction box

- fuse box

- A valve which is placed in a water or gas service pipe of a building near its junction with the public wate main

- meter

- corporation cock

- gate valve

- water main

- The rate at which electricity flows in the same direction

- ampere

- electric current

- coulomb

- Electric current which always flows in the same direction

- direct

- alternating current

- drop

- The force that makes electron move in a circuit

- resistance

- electromotive force

- electric power

- The ratio of output into input

- capacitance

- efficiency

- power factor

- Opposes the change in magnitude of an alternating current and makes the current lag the voltage

- inductance

- frequency

- cycle

- A large single panel frame or assembly of panels in the form of a single panel

- panelboards

- switchboards

- service entrance

- The unit of the quantity of light

- foot-candle

- lumen

- candle power

- Connection which were merely pushed onto the conduit

- slip connection

- pin grip

- loop system

- Heat flows to a cooler surface through space in the same way in which light travels

- convection

- radiation

- conduction

- Materials used to stop the transfer of heat

- caulking

- insulation

- water stripping

- Heat is produced when electricity passes through resistance wires

- solar heat

- electric heat

- steam heat

- Blanket insulation consists of materials made of

- thin sheets

- flexible sheets

- rigid sheets

- In this heating system, the main loss of heat is through the windows outside the walls.

- perimeter

- radiant

- concentrated

- A device that keeps the house at a constant temperature regardless of the loss of heat through walls.

- regulator

- compressor

- thermostat

- A system that takes the moisture from the damp air and passes it over cold coils.

- heating

- humidification

- ventilation

- Air-conditioning system absorbs the heat from the house and transfers it to a liquid refrigerant called

- carbo

- freon

- steam

- A component of elevator, consisting of a flyball device designed to stop an elevator if the speed becomes excessive

- modulators

- conductors

- governors

- A mechanical system consisting of a boiler, water-circulating piping and pump and radiators.

- hydronic

- tractive

- resistive

- A cylindrical device that turns on an axis around which a firehose is wound and connected.

- radiant

- hose reel

- drum

- An electric friction that tends to prevent electrical current from passing through a wire

- resistance

- short circuit

- convection

- The process of treating air so as to control simultaneously its temperature, humidity, cleanliness and distribution to meet the requirements of the conditioned space.

- air-conditioning

- humidification

- filtering

- A mechanical device for the purpose of increasing the pressure upon the refrigerant

- condenser

- compressor

- evaporator

- A fitting joining two pipes at an angle

- bend

- elbow

- nipple

- A passageway made if sheet metal or other suitable material, leak-tight for conveying air or other gases at low temperature

- piping

- ducting

- raceway

- The part of the AC/refrigerant system in which liquid refrigerant is vaporized to produce refrigeration

- condenser

- evaporation

- ventilation

- A substance which produces a refrigerating by effect by its absorption of heat while expanding or evaporating

- boiler

- refrigerant

- condenser

- A receptacle in which liquids are retained for a sufficient time to permit the deposition and retention of sediment in the basin

- catch basin

- area drain

- sludge pit

- Heating, ventilating and air-conditioning is abbreviated as

- HVAC

- HVAAC

- HVA

- As to the Building Code of the Philippines, under the Rule X, refrigerant piping crossing a passageway in any building shall have a height no less than

- 2.40 meters

- 2.30 meters

- 2.10 meters

- Window type ACU shall be provided with a way to discharge its condensed water into a suitable container by means of

- drain pipe

- plastic tubing

- both

- any

- Window type ACU installed on the ground floor of buildings shall not be less than

- 2.10 meters

- 2.13 meters

- 2.20 meters

- Window type ACU shall be provided with a way to exhaust its discharge into the corridors, hallways, arcades and sidewalks by means of

- exhaust ducts

- condenser

- roof vents

- Window type ACU installed along corridors, hallways, above the first floor shall not be less than the ____ above the floor level

- 2.10 meters

- 2.13 meters

- 2.20 meters

- One of which is not equivalent to the normal body temperature

- 37 degrees Celsius

- 98.6 degrees Fahrenheit

- 67 degrees Celsius

- What does ASHRAE stand for?

- American Society of Heating, Refrigeration and Air-conditioning Engineers

- Association of Heating, Refrigeration and Air-conditioning Engineers

- Association of Heating and Refrigeration American Engineers

- As per the Building Code of the Philippines, the temperature and humidity of the air to be used for comfortable cooling shall be maintained at

- 68-74 degrees Fahrenheit

- 54-69 degrees Fahrenheit

- 71-75 degrees Fahrenheit

- To compute for the air volume, the unit of measurement is cubic feet per minute or cubic minute indicated in the abbreviations of

- cfm and cm

- cu. ft/m and cu. m./mm.

- both a and b

- Measurable environment is one category that affects comfort, one under, which is the

- air temperature

- total cooling capacity

- metabolism

- Personal or physical factors is one category that affects comfort, one of which is

- air temperature

- total cooling capacity

- metabolism

- The basic component like door, window, wall and roof or the transition space between inside to outside is referred to in this subject as

- skin of the building

- building envelope

- fenestration

- A general freight leading has a rating in net are of the platform of

- 50 psf

- 45 psf

- 90 psf

- A dumbwaiter has a limited area and height of

- 9 sq. ft. area and 4 ft. height

- 18 sq. ft area and 9 ft. height

- no limited height, depends upon the design

- A vertical transportation for cargoes is

- freight elevator

- hydraulic elevator

- passenger elevator

- A type of elevator for the purpose of providing a spectacular unit usually glass enclosed outside of the building or inside malls

- slant elevator

- observation car elevator

- hydraulic elevator

- The maximum height a moving walk can extend is

- 300 meters

- 320 meters

- 365 meters

- A type of elevator having 2 decks and can discharge into 2 succeeding floors at one time

- double-deck elevator

- skyplaza elevator

- multi-level elevator

- An electric passenger escalator having a size of 48 inches and a tread width of 40 inches has a maximum passenger per hour rating of

- 5200 passengers

- 9000 passengers

- 7300 passengers

- A moving ramp has a maximum inclination of

- 50 psf

- 45 psf

- 90 psf

- One significant purpose of a moving ramp is

- To move persons who lack the agility required to use the escalator

- To delay the impact of heaving traffic flow

- To minimize the loading requirements of an elevator

- The dimension of “OH” is based on the overall height of elevator car which is

- 8 ft. 4 inches

- 6 ft. 4 inches

- 7 ft. 2 inches

- Average strength of prestressed concrete

- 4000 psi

- 5000 psi

- 6000 psi

- 7000 psi

- Critical period of concrete where it loses its moisture

- first 3 days

- first 5 days

- first 7 days

- first 10 days

- Lumber less than 4” in width and less than 2” in thickness

- furring

- ledger

- strip

- board

- Which is not a brand name of Portland cement?

- Dragon

- Universal

- Rizal

- Filipinas

- Brand name of plastic roofing

- Metalplas

- Plastech

- Adplas

- Kveco

- Undried or unseasoned wood

- green lumber

- sap lumber

- timber

- xylem

- Which is NOT a company of pest control?

- Rentokil

- Dorma

- Timberpro

- Mapelon

- Which is NOT a brand name of skylight roofing?

- Lexan

- Danpalon

- Luxalon

- Hi-corr

- Which is NOT a brand name of laminated flooring?

- Pergo

- Bruce

- Magellan

- Kendall

- Which of the following is an elastomeric paint?

- Flexseal

- Superseal

- Acrybond

- Tilestik

- Which of the following is cementitious water-proofing?

- Flexseal

- Superseal

- Acrybond

- Ceramicoat

- Which of the following is an insulating elastomeric paint?

- Flexseal

- Superseal

- Ceramicoat

- Tilestik

- Which of the following is a water-proof tile adhesive and grout?

- Tilestik

- Acrybond

- Flexseal

- Ceramicoat

- Kilogram weight per square meter of load-bearing CHB with plaster

- 250 kg./sqm

- 285 kg./sqm

- 325 kg./sqm.

- 375 kg./sqm.

- Kilogram weight of steel reinforced concrete (SRC) panel with plaster

- 175 kg./sqm

- 183 kg./sqm.

- 225 kg./sqm.

- 150 kg./sqm.

- Which is NOT part of a T-runner suspended ceiling system?

- main tee

- cross tee

- wall angle

- furring

- Which one is NOT a quality of an IMAC roof?

- 15 microns regular polyester

- shock-proof

- thermoplastic resins

- built-in insulation

- An efficient substitute for costly wood panel

- Spanflex

- Pergo

- Hi-corr

- Kendall

- Flexible method of controlling subsurface water

- drilling

- well-pointing

- dredging

- trenching

- In masonry, any bond in which the vertical joists are precisely in line

- plummet

- plunger

- ridge cut

- pluteus

- Process which takes place at constant temperature

- exothermic

- isothermal

- isotropic

- endothermic

- Kind of brick bond mortar used for rough surface

- stripped

- raked

- strucked

- v-cut

- A principal repeated element in an ornamental design

- intricacy

- motif

- mouchette

- design concept

- Material used to build up the core of a larger plaster molding

- muffle

- mud slab

- mudsill

- mow

- A travelling support for concrete forms

- jumpover

- jumbo

- stationery

- joist jack

- A small hole in a door for watching, as in prison door

- jube

- judas

- joggle

- chisel

- A projecting part of a building

- jib

- jim

- jetty

- gabbro

- A cornice

- gatch

- geison

- gabbro

- jib

- The horizontal base course of masonry on the ground

- ground coat

- ground coarse

- ground cover

- ground plane

- A small tool with pointed screw at one end

- brad

- gimmer

- girandole

- gimlet

- Concrete should not be left exposed for more than

- 1/2 hour

- 1 hour

- 1 1/2 hours

- 2 hours

- Concrete vibrations should be put in location of pouring for not more than

- 5 seconds

- 10 seconds

- 20 seconds

- 30 seconds

- Projections on the sides of steel that provides greater bonding between concrete and steel

- slug

- lugs

- patina

- dowel

- Concrete slab on fill shall be poured on a stable base of not less than ___ thick

- 50 mm

- 100 mm

- 150 mm

- 175 mm

- Each concrete slab course to be poured shall not be more than ___ meter wide.

- 1 meter

- 1.50 meters

- 2.0 meters

- 0.5 meter

- Compound to be poured before doing construction joints

- paste

- grout

- hydraulic grout

- scratch grout

- Reactive resins product for floor finishes

- boral

- silikal

- segovia

- karl

- Which is NOT a characteristic of gypsum board?

- thermal insulation

- sound control

- washable

- sag resistant

- T-joist floor system is manufactured by

- Jackbilt

- Custombilt

- Freyssinet

- Prescon

- T-joist floor and roof system is a

- prestressed

- cast-in-place

- post-stressed

- prefabricated

- Polymers modified fiber cement (PMFC) is manufactured by

- Quantum

- Riviera

- Bucino

- Re-con

- Which is NOT included in a composition of PMFC?

- cemtitious materials

- cyloxide?

- cellulose fiber

- polyethelene

- Used to fasten metal stud to concrete

- jetty

- tucker

- ramset

- silent rod

- Project manager’s representative on the jobsite

- assistant project manager

- resident manager

- site manager

- site supervisor

- A board of arbitrators is composed of ___ members

- 3

- 5

- 2

- 7

- Refers to a general accomplishment in construction at a point in time

- CPV

- event

- milestone

- gnatt

- Method of laminating a particle board and the like to enhandle surface appearance

- HPD

- FGM

- DPL

- GFRC

- A modified septic anaerobic filter tank

- sewage treatment plant

- chlorination tank

- microbe disinfection system

- biogreen tank

- A metal plastic eyelet which provides a reinforced hole for attachment

- groin

- grit

- griffe

- grommet

- Also known as N-truss

- Pratt

- Fink

- Warren

- Petit